The Introduction of the network control-signal Lighting Arrester

## Type AC9913

## The Functions and Characteristics.

The range of POW021 lighting arrester is used for protecting the sensitive high speed network communication circuits. It is widely used for protecting data transmission system in computer communication, network switchboard and network router from serious damage, which made by thunder and lightning induced tension, electrical network voltage undulation disturbance, static discharge, and impact surge voltage.

Its main characteristics are;

- Using multilevel protection circuit.

- Choosing the famous international brand products as central components. Reliable high quality, made by state-of-the-art technology and equipment.

(2) It has great flow capacity, low-level persistent voltage, sensitive reaction, steady capability, and low-loss insert.

2. The Parameters of the Product

| Type | AC9913 |
| --- | --- |
| Continuous operating voltage Un | 5V |
| Maximum working voltage Uc | 10V |
| Nominal discharging current In(8/20us) | 5KA |
| Maximum discharging voltage Imax（8/20us） | 10KA |
| Limit voltage Up | 15V |
| Data transmission rate Vs | 100Mbps |
| Insert loss Ae | 0.2dB |
| Corresponsive time Ta | 1nS |
| Joint form | RJ45 |
| Protection form | 1、2、3、6 |
| Working conditions | Temperature -25—+65℃；Humidity≤95%（25-30℃） |
| Test standard | IEC61643-21：2000 |

3. Installation and Maintenance

- The lighting arrestor is linked between the access of signal and the protected equipment.

- The input of the lighting arrestor should connect the protected equipment, the output should connet with the protected equipment,do not connect in the opposite direction.

- The PE line of the lighting arrestor must strictly be connected to the lighting protection system at the equipotential, or, it will influence the operating function.

- This product need not pay special attention to maintain, but it should be installed close to the equipment’s port as possible as you can. When the operating system goes wrong, please check the lighting arrestor after removing it. If the lighting arrestor recovers by restoring it to unused condition, please change the lighting arrestor.

4.The example picture of installation.

Connect the signal line